## Slide 1: Introduction to
Classification and labelling of mixtures
Wednesday 12. aug. 2020 09:15 – 15.00
Auditorium 1, Chemistry building
Karoline Fægri og Svein Tveit, Skolelaboratoriet i kjemi

## Slide 2: Competence aims
Enable students to:
Be aware of the regulations that apply to classification and labelling of chemicals
Explain some fundamental concepts used in classification and labelling of hazardous substances and mixtures
Explain the elements of CLP hazard labelling
Label aquatic solutions of 2 mol/L NaOH, 15 % HCl, 9 % NH3 and 0,2 mol/L CuSO4
Notes: Downstreams user?

## Slide 3: Outline
Background information on CLP
Definitions and rules used in classification and labelling with CLP
Example 1 - how to make a label
Exercise 1 & 2
More definitions and rules
Example 2 - how to make a more difficult label
Exercise 3 & 4
How do we label chemicals at the university

## Slide 4: Breaks
10.10 – 10.30
11.30 – 12.15 – lunch

## Slide 5: Outline
Background information on CLP
Definitions and rules used in classification and labelling with CLP
Example – how to make a label
Exercise 1 & 2
More definitions and rules
Example 2 - how to make a more difficult label
Exercise 3 & 4
How do we label chemicals at the university

## Slide 6: Why is it important to classify and label chemicals?

## Slide 7: HSE/HMS – authorities in Norway
 | Nature of hazards | Resposible authorities for HSE-laws and regulations
Health Helse | Health | Norwegian Labour Inspection Authority Arbeidstilsynet
Safety Sikkerhet | Physical | Norwegian Directorate for Civil Protection Direktoratet for samfunnssikkerhet og beredskap (DSB)
Environment Miljø | Environment | Norwegian Environment Agency Miljødirektoratet

## Slide 8: About Regulation (EC) No 1272/2008 (CLP)
GHS | Global Harmonized System for classification and labelling of chemicals FNs globalt harmoniserte system for klassifisering og merking av kjemikalier
ECHA | European CHemicals Agency, responsible for implementing GHS in EU by establishing and updating an inventory for GHS substances Det europeiske kjemikaliebyrået ECHA har ansvar for å etablere og holde oppdatert et register over stoffers fareklassifisering og -merking.

## Slide 9: About Regulation (EC) No 1272/2008 (CLP)
REACH | Regulation (EC) No 1907/2006 Registration, registrering Evaluation, vurdering Authorisation and Restriction, godkjenning og begrensning CHemicals, kjemikalier
CLP | Regulation (EC) No 1272/2008 Classification. klassifisering Labelling, merking Packaging of Substances and Mixtures, og emballering av stoffer og stoffblandinger

## Slide 10: Timeline for implementing CLP
1. December 2010
CLP in EU
16. June 2012
CLP in Norway
Old labels and CLP until
1. June 2015
only CLP after
1. juni 2017
Kilde: http://www.miljodirektoratet.no/Global/dokumenter/tema/kjemikaler/reach_clp_tidslinje_800.jpg (august 2014)
Notes: Forskrift om klassifisering, merking og emballering av stoffer og stoffblandinger (CLP) ble innført 16. juni 2012. Denne forskriften erstatter Forskrift om klassifisering, merking mv. av farlige kjemikalier (Merkeforskriften).
Skal sikre samme merking for lagring, omsetning og transport, over hele verden.

## Slide 11
Product identifier
Hazard pictogram
Signal word
Hazard statement
Precautionary
statement
Company identity
Hazard communication

## Slide 12: Product identifier
Name and identification number given in the Classification and Labelling Inventory
if not included in C&L Inventory
CAS number and IUPAC name

## Slide 13: Hazard classes and categories (not part of labelling)

## Slide 14: Hazard pictograms
Health
Physical
Environment

## Slide 15: Signal words and hazard statements

## Slide 16: Groups of hazard and precautionary statements
Code | hazard statements | Code | precautionary statements
H200-H299 | Physical | P100-P199 | General
H300-H399 | Health | P200-P299 | Prevention
H400-H499 | Environment | P300-P399 | Response
 |  | P400-P499 | Storage
 |  | P500-P599 | Disposal
EUH | only in the EU |  | 

## Slide 17: Example 1 – Classifying and making labels
Label 3 mol/L H2SO4 1 L bottle

## Slide 18
Sulfuric acid, 3 mol/L H2SO4
CAS nr.
Label
Classification
Notes: Concentration: 3 mol/L * 82 g/mol = 246 g/L In mass %: 246 g/L / 1170 g/L * 100% = 21 % (m/m

## Slide 19: Exercise 1
1a) Make a label for 2 mol/L NaOH
1b) (optional) Make a label for 5 mol/L HCOOH (density 1,05 g/mL)

## Slide 20
Natriumhydroksid 2 mol/L NaOH
CAS nr. 1310-73-2
Fare
Gir alvorlige etseskader på hud og øyne.
Benytt øyevern. VED HUDKONTAKT (eller håret): Tilsølte klær må fjernes straks. Skyll huden med vann. VED KONTAKT MED ØYNENE: Skyll forsiktig med vann i flere minutter. Fjern eventuelle kontaktlinser dersom dette enkelt lar seg gjøre. Fortsett skyllingen. Kontakt umiddelbart et GIFTINFORMASJONSSENTER eller lege.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Laget av Svein Tveit 09.08.2019

## Slide 21
Sodium hydroxide 2 mol/L NaOH
CAS nr. 1310-73-2
Danger
Causes severe skin burns and eye damage.
Wear eye protection. IF ON SKIN (or hair): Take off
immediately all contaminated clothing. Rinse skin with water. IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Immediately call a POISON Center or doctor.
Department of Chemistry, Sem Sælandsvei 26, Oslo, 22855536
Made by Svein Tveit 09.08.2019

## Slide 22
Maursyre 5 mol/L HCOOH
CAS nr. 64-18-6
Fare
Gir alvorlige etseskader på hud og øyne.
Benytt øyevern. VED HUDKONTAKT (eller håret): Tilsølte klær må fjernes straks. Skyll huden med vann. VED KONTAKT MED ØYNENE: Skyll forsiktig med vann i flere minutter. Fjern eventuelle kontaktlinser dersom dette enkelt lar seg gjøre. Fortsett skyllingen. Kontakt umiddelbart et GIFTINFORMASJONSSENTER eller lege.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Laget av Svein Tveit 09.08.2019
Formic acid 5 mol/L HCOOH
CAS nr. 64-18-6
Danger
Causes severe skin burns and eye damage.
Wear eye protection. IF ON SKIN (or hair): Take off
immediately all contaminated clothing. Rinse skin with water. IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Immediately call a POISON Center or doctor.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Made by Svein Tveit 09.08.2019

## Slide 23: Exercise 2
2a) Make a label for 15 % HCl
2b) (optional) Make a label for 7,7 % H2O2

## Slide 24
Saltsyre 15 % HCl
CAS nr. 7647-01-0
Advarsel
Irriterer huden.
Gir alvorlig øyeirritasjon.
Kan forårsake irritasjon av luftveiene.
Benytt øyevern. Unngå innånding av gass. Vask hendene grundig etter bruk. Ved vedvarende øyeirritasjon: Søk legehjelp. Kontakt et GIFTINFORMASJONSSENTER eller lege ved ubehag.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Laget av Svein Tveit 09.08.2019

## Slide 25
Hydrochloric acid 15 % HCl
CAS nr. 7647-01-0
Warning
Causes skin irritation.
Causes serious eye irritation.
May cause respiratory irritation.
Wear eye protection. Avoid breathing gas. Wash hands thoroughly after handling.If eye irritation persists: Get
medical advice/attention. Call a POISON CENTRE or doctor if you feel unwell.
Department of Chemistry, Sem Sælandsvei 26, Oslo, 22855536
Made by Svein Tveit 09.08.2019

## Slide 26
Hydrogenperoksid 7,7 % H2O2
CAS nr. 7722-84-1
Advarsel
Gir alvorlig øyeirritasjon.
Benytt øyevern. Ved vedvarende øyeirritasjon:
Søk legehjelp.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Laget av Svein Tveit 09.08.2019
Hydrogen peroxide 7,7 % H2O2
CAS nr. 7722-84-1
Warning
Causes serious eye irritation.
Wear eye protection. If eye irritation persists: Get
medical advice/attention.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Made by Svein Tveit 09.08.2019

## Slide 27: Concentration limits
Specific concentration limits and Generic concentration limits

## Slide 28: Classification for acute or chronic aquatic hazard
L(E)C50 from SDS
SECTION 12: Ecological information
12.1. Toxicity
Acute aquatic, fish: Value: x mg/l

## Slide 29: M - factor

## Slide 30: Classification – Aquatic acute

## Slide 31: Classification – Aquatic chronic

## Slide 32: Classification – Acute toxicity
ATE = Acute toxicity estimate

## Slide 33: Acute toxicity
Example
A 5 % solution of a substance classified as acute tox. 3 – oral exposure

## Slide 35: Acute toxicity
Example
A 5 % solution of a substance classified as acute tox. 3 – oral exposure

## Slide 36: Example 2 – Classifying and making labels
Label 4 mol/L ZnCl2 in 1 L bottle
(density 1,4 g/mL)

## Slide 37
Zinc chloride, 4 mol/L ZnCl2
CAS nr.
Label
Classification
Notes: Concentration: 4 mol/L * 136 g/mol = 544 g/L In mass %: 544 g/L / 1400 g/L * 100% = 39 % (m/m)
M = 1

## Slide 38: Exercise 3
3a) Make a label for 9 % NH3 in 1L bottle
3b) (optional) Make a label for 0,3 mol/L HNO3

## Slide 39
Ammoniakk 9 % NH3
CAS nr. 1336-21-6
Fare
Gir alvorlige etseskader på hud og øyne. Kan forårsake irritasjon av luftveiene.
Benytt øyevern. Unngå innånding av gass. VED HUDKONTAKT (eller håret): Tilsølte klær må fjernes straks. Skyll huden med vann. VED KONTAKT MED ØYNENE: Skyll forsiktig med vann i flere minutter. Fjern eventuelle kontaktlinser dersom dette enkelt lar seg gjøre. Fortsett skyllingen. Kontakt umiddelbart et GIFTINFORMASJONSSENTER eller lege.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Laget av Svein Tveit 09.08.2019

## Slide 40
Ammonia 9 % NH3
CAS nr. 1336-21-6
Danger
Causes severe skin burns and eye damage. May cause respiratory irritation.
Wear eye protection. Avoid breathing gas. IF ON SKIN (or hair): Take off immediately all contaminated clothing. Rinse skin with water. IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Immediately call a POISON Center or doctor.
Department of Chemistry, Sem Sælandsvei 26, Oslo, 22855536
Made by Svein Tveit 09.08.2019

## Slide 41
Salpetersyre 0,3 mol/L HNO3
CAS nr. 7697-37-2
Advarsel
Irriterer huden.
Gir alvorlig øyeirritasjon
Benytt øyevern. Vask hendene grundig etter bruk. Ved vedvarende øyeirritasjon: Søk legehjelp.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Laget av Svein Tveit 09.08.2019
Nitric acid 0,3 mol/L HNO3
CAS nr. 7697-37-2
Warning
Causes skin irritation.
Causes serious eye irritation.
Wear eye protection. Wash hands thoroughly after handling. If eye irritation persists: Get medical advice/attention.
Department of Chemistry, Sem Sælandsvei 26, Oslo, 22855536
Made by Svein Tveit 09.08.2019

## Slide 42: Exercise 4
4a) Make a label for 0,2 mol/L CuSO4
4b) (optional) Make a label for 1 mol/L ZnCl2

## Slide 43
Kobber(II)sulfat, 0,2 mol/L CuSO4
CAS nr. 7758-98-7
Giftig med langtidsvirkning for liv i vann
Unngå utslipp til miljøet. Samle opp spill.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Laget av Svein Tveit 09.08.2019

## Slide 44
Copper(II)sulfate, 0,2 mol/L CuSO4
CAS nr. 7758-98-7
Toxic to aquatic life with long lasting effects.
Avoid release to the environment. Collect spillage.
Department of chemistry, Sem Sælandsvei 26, Oslo, 22855536
Made by Svein Tveit 09.08.2019

## Slide 45
Sinkklorid 1 mol/L ZnCl2
CAS nr. 7646-85-7
Fare
Gir alvorlige etseskader på hud og øyne. Kan forårsake irritasjon av luftveiene.
Giftig, med langtidsvirkning, for liv i vann.
Benytt øyevern. Unngå innånding av gass. VED HUDKONTAKT (eller håret): Tilsølte klær må fjernes straks. Skyll huden med vann. VED KONTAKT MED ØYNENE: Skyll forsiktig med vann i flere minutter. Fjern eventuelle kontaktlinser dersom dette enkelt lar seg gjøre. Fortsett skyllingen. Kontakt umiddelbart et GIFTINFORMASJONSSENTER eller lege. Unngå utslipp til miljøet. Samle opp spill.
Kjemisk institutt, Sem Sælandsvei 26, Oslo, 22855536
Laget av Svein Tveit 09.08.2019
Zinc Chloride 1 mol/L ZnCl2
CAS nr. 7646-85-7
Danger
Causes severe skin burns and eye damage. May cause respiratory irritation.
Toxic to aquatic life with long lasting effects.
Wear eye protection. Avoid breathing gas. IF ON SKIN (or hair): Take off immediately all contaminated clothing. Rinse skin with water. IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. Immediately call a POISON Center or doctor. Avoid release to the environment. Collect spillage.
Department of chemistry, Sem Sælandsvei 26, Oslo, 22855536
Made by Svein Tveit 09.08.2019

## Slide 46: Harmonised classification
Harmonised classification (as provided in Annex VI to CLP), must always be used by a manufacturer
Harmonised classification normally applies to those properties of the highest concern
Where some, but not all hazard classes or differentiations within hazard classes have been harmonised, the remainder should be self-classified to complete the classification
Guidance on the Application of the CLP Criteria

## Slide 47: Leads to different classification for the same mixture
Ammonia 25 % (Avantor)
Skin corrosion 1B
Aquatic acute, 1
STOT, SE, 3
Serious eyedamage, 1
Aquatic chronic, 2
Ammonia 25 % (Merck)
Skin corrosion, 1B
Aquatic acute, 1
STOT, SE, 3
Corrosive to metals, 1

## Slide 48: CLP in scientific research
This Regulation (CLP) shall not apply to the following:
substances and mixtures for scientific research and development, which are not placed on the market, provided they are used under controlled conditions in accordance with Community workplace and environmental legislation.
http://eur-lex.europa.eu/LexUriServ/LexUriServ.do?uri=OJ:L:2008:353:0001:1355:en:PDF
Title 1, Article 1, 2d

## Slide 49: How to label mixtures in your science lab
Mixtures that are to be use the same day do not require any labelling
Mixtures that are left over night requires a minimum labelling of:
  Name and molar concentration
  Hazard pictograms
  Hazard statements
  Highly relevant precautionairy statements

## Slide 50: Evaluation
Plus, minus, delta